PART A: INFORMATION FOR THE TENDERER

Name and address of the contracting authority: Territorial Administrative Unit Moldova Noua City, N. Balcescu str., no. 26, Moldova Noua city, Caras-Severin county, Romania Title of the tender: Soil and water testing equipment Reference number: 6/RORS365/Local Council of Moldova Noua Date of launching: 19/03/2020

- INFORMATION ON SUBMISSION OF THE TENDERS

Subject of the contract:

The subject of this tender is:

- Provision of supplies as indicated in the technical information in the point 2 of these information - Soil and water testing equipment

Deadline for submission of the tenders:

The deadline for submission of tenders is 30/03/2020 at 16:00 hours. Any tender received after this deadline will be automatically rejected.

* - The tenderer should have minimum 7 days from the date of launching of the procurement procedure for preparation of the offer (excluding the day of publishing and the date of submission deadline).

** - The Contracting Authority is obliged to provide answer to all questions received no latter then 3 days before the deadline and has to publish them on the same web sites where the tender was published.

Currency

Tenders must be presented in Euro.

Award criteria:

# The sole award criterion will be the price. The contract will be awarded to the lowest compliant tender.

In case that one offer is received, the Contracting Authority shall check whether the offer is administratively and technically compliant with the requirements set by this tender documentation and financial offer is within the available budget.

Variant solutions will not be taken into consideration.

Award notification

The successful tenderer will be informed of the results of the evaluation procedure in written form.

Contract award notice will be published on the programme website. The estimated time of communication publishing of results to the tenderers is 7 days after the date of contract signature.

Address and meanings for submission of the tenders:

The tenderers will submit their tenders using the standard submission form available in the “Part B: Format of offer to be provided by the tenderer” of the tender dossier. The tender will be submitted in 1 original. Any tenders not using the prescribed form may be rejected by the contracting authority.

In addition to the offer the tenderer is required to provide the following supporting documentation:

- Copy of legal registration*only for Romanian beneficiaries (only if not publicly available for Contracting Authority to consult)

- <any other documents requested by Contracting Authority>

The tenders will be submitted in a sealed envelope, containing the following information:

- Name and address of the tenderer

- Title of the tender: Soil and water testing equipment

- Reference number: 6/RORS365/Local Council of Moldova Noua

- The words: ‘’Not to be opened before the tender opening session’’ (and ‘’Ne otvarati pre sastanka za otvaranje ponuda’’ /“A nu se deschide inainte de sesiunea de deschidere”)

The tenders will be submitted in person, by post or courier service to the following address:

Territorial Administrative Unit Moldova Noua City, N. Balcescu str.,  no. 26, Moldova Noua city, Caras-Severin county, Romania,

Contact person: Stâncă Narcis

Mail contact: pmn_invest@yahoo.com

The tenderers are reminded that in order to be eligible the tenders need to be received by the Contracting Authority by the deadline indicated above.

- TECHNICAL INFORMATION

The tenderers are required to provide supplies as indicated below. In the tenderer’s technical offer, the tenderers might indicate more details on the deliveries, including brand names if applicable, referring back to the below table.

| No. | Number of items | Title of item | Technical specifications |
| --- | --- | --- | --- |
| Supplies |
| 1.1. | 100 tests | Arsenic 50 test | 0 - 3,0 mg/l As³⁺/As⁵Modified Gutzeit test |
| 1.2. | 100 tests | Nitrate100 test strips, nitrate/ nitrite | yellow - red-violetNitrate: 0 - 100 mg/l NO₃⁻Nitrite: 0 - 50 mg/l NO₂⁻ Modified Griess reaction |
| 1.3. | 100 tests | Test strips, chromate, | Chromate 0 - 100 mg/l CrO⁴₂- Carbazide |
| 1.4. | 100 tests | Test strips, ammonium, Ammonium | 0 - 400 mg/l NH₄+ Nessler |
| 1.5. | 100 tests | Test strips, tin | Tin 0 - 500 mg/l Sn₂+ Phosphomolybdic acid |
| 1.6. | 100 Tests | Test strips, cobalt | Cobalt 0 - 1000 mg/l Co₂+ Rhodanid |
| 1.7. | 100 tests | Test strips, total iron, | Total iron test strips, white - dark red 0 - 1000 mg/l Fe²⁺/Fe³⁺ 2,2'-Bipyridine |
| 1.8. | 100 Tests | Test strips, molybdenum | Molybdenum 0 - 250 mg/l Mo⁶+ Dithiol |
| 1.9. | 100 Tests | Test strips, nickel, | Range: 0 - 1000 mg/l Ni₂+ |
| 1.10. | 100 Tests | Zinc test sticks | Range: 0 - 100 mg/l Zn₂+ 6x95mm incl. reagents |
| 1.11. | 100 Tests | Test strips, Nitrate, | Nitrate: 0 - 100 mg/l NO₃⁻ Nitrite: 0 - 50 mg/l NO₂⁻ |
| 1.12. | 100 Tests | Copper test sticks 6x95mm | Range: 0 - 300 mg/l Cu+/₂+ |
| 1.13. | 40 tests | Test paper, qualitative, Plumbtesmo® Packaging: Pack of 40 sheets 40×25 mm | The test paper allows the quick and easy detection of lead (Pb) on surfaces including metal surfaces, dishes, ceramics and toys. In criminal investigations it is used to search for traces of bullets. Colour change: White-yellow to pink The surface in question is moistened with distilled water. The test paper is pressed against the surface for about two minutes. In the presence of Lead the paper turns pink to dark purple. Limit of sensitivity: 5 mg/l |
| 1.14. | 100 tests | pH indicator test strips, | pH-Fix pH-Fix, not CE marked 0 - 14 |
| 1.15. | 100 tests | Test strips, water hardness | strips (6×95 mm) 54 - 450 mg/l CaCO₃ 100 |
| 1.16. | 70 tests | Colorimetric Rapid Tests, Manganese, |  |
| 2.1. | 1 piece | Laboratory heat insulation bag | Dimensions: min 28 x 47 x 22 cm Weight: min 2.86 kg. Material: Polyamide. Washable. |
| 2.2. | Set of 6 pieces | Berzelius low PMP form | Material: PMP / TPX (polymethylpentene) High transparency Chemical and thermal resistance greater than PP Easy to read, embossed gradations See ISO 7056: 1981 Capacity: 250 ml Gradations: 25 ml Diameter: 83.1 mm Height: 92.1 mm |
| 2.3. | 3 pieces | 250 ml graduated cylinder, class B, PMP | Material: PMP / TPX (poly methylpeentene) Greater transparency, better chemical and thermal resistance than PP autoclave Easy to read, gradations easily embossed See ISO 6706 Capacity: 250 ml Gradations: 2 ml Accuracy: ± 2 ml Diameter: 40.15 mm Height: 326.5 mm |
| 2.4. | 500 pieces | Sealing bag | Dimensions: 150x220 mm Material: PP |
| 2.5. | Set of 6 pieces | The measuring rod With gradations | Autoclavable at 121 degrees C Capacity: 500 ml Gradations: 25 ml |
| 2.6. | 300 pieces | Sample container with PP screw cap | autoclave Capacity: 150 ml Base diameter: 52 mm Cover diameter: 58 mm Height: 80 mm Grading: from 10 in 10 ml to 120 ml |
| 2.7. | 100 pieces | Sterile syringe, individually packaged | consisting of two parts Luer Cone Capacity: 10 ml according GMP, ISO 9000, DIN 13097 – 13099 |
| 2.8. | 5 pieces | Chattaway spatula | Length: 200 mm Material: stainless steel |
| 2.9. | 20 pieces | Laboratory glass with lid according ISO 4796, graded, transparent | Material: borosilicate glass LBG 3.3 Totally autoclavable With blue threaded cap Capacity: 500 ml Base diameter: 86 mm Height: 176 mm Capacity: GL 45 |

Delivery conditions: the delivery is made at the beneficiary's place – Moldova Noua, all the costs of transporting the equipment to the beneficiary's place fall to the supplier / tenderer.

The equipment must be accompanied by warranty certificates, compliance statements, model approval certificates and initial verification bulletins (if applicable), operating manuals.

The training of the user personnel is performed free of charge at the beneficiary's place.

NOT TO BE FILED IN BEFORE CONTRACT SIGNING NOT TO BE SUBMITTED WITHIN THE OFFER!!!

FORMAT OF THE CONTRACT BETWEEN THE CONTRACTOR AND THE CONTRACTING AUTHORITY

CONTRACT TITLE: Soil and water testing equipment

REF: 6/RORS365/Local Council of Moldova Noua

Concluded between:

<Title>

<Address of the contracting authority>

(Contracting Authority)

AND

<Title>

<Address of the contractor>

Official registration number/ VAT number>

(Contractor)

Article 1: Subject of the contract

The subject of the contract is the supplies as indicated in the contractor’s offer – ‘’Part B: Format of offer to be provided by the tenderer’’.

Article 2: Contract value

The total contract value for implementation of delivery of supplies indicated in the Article 1 is: <XXX EUR/National currency>.

For Serbian partners:

The contract shall be exempt from all duties and taxes (including VAT and custom taxes).

For Romanian Partners:

In accordance with IPA implementing regulation for Romanian partners, VAT can be an eligible expenditure if the VAT is clearly identified on the invoices.

Article 3: Contracting documents

The documents which form the part of this contract are (by the order of precedence):

- Contract agreement

- Contractor’s offer as provided in the tendering phase – ‘’Part B: Format of offer to be provided by the tenderer’’

- Any other supporting documentation if applicable (* - in case of asking for registration of company or other information)

For any issues not defined in this contract agreement the rules of General conditions will be applied

| C4e | Draft contract : General conditions (Annex I) | c4e_annexigc_en.pdf |
| --- | --- | --- |

http://ec.europa.eu/europeaid/prag/document.do?isAnnexes=true

Article 4: Deliveries and payments

The contractor will deliver without reservation the supplies indicated in the contractor’s offer ‘’Part B: Format of offer to be provided by the tenderer’’. The deliveries will be implemented within the indicated dates.

The Contracting Authority will pay to the contractor the supplies in the amount indicated in the Article 2 of this contract document.

In case the contract is concluded in EURO, and payments are made in national currencies, applicable exchange rate must be InforEuro exchange rate for the month of the issuing of invoice or pre-invoice in case of VAT exemption.

The payments will be issued by the following time schedule.

| Day/Month |  | <EUR/RSD> |
| --- | --- | --- |
| < Day/Month > | Interim payment (if applicable) | <XX % of the contract value / Absolute amount > |
| < Day/Month > | Balance final payment | < XX % of the contract value / Absolute amount > |
|  | Total | <Total contract value> |

Article 5: Duration of the contract

The duration of the contract is < XX days/months >.

Commencement date is <dd/mm/yyyy>

Article 6: Resolving of disputes

Any disputes arising out of or relating to this Contract which cannot be settled otherwise shall be referred to the exclusive jurisdiction of (* - specify responsible court or arbiter body) in accordance with the national legislation of the state of the Contracting Authority.

| For the Contractor | For the Contracting Authority |
| --- | --- |
| Name: |  | Name: |  |
| Title: |  | Title: |  |
| Signature: |  | Signature: |  |
| Date: |  | Date: |  |

PART B: FORMAT OF OFFER TO BE PROVIDED BY THE TENDERER

Title of the tender: Soil and water testing equipment Reference number: 6/RORS365/Local Council of Moldova Noua

- TENDERER’S INFORMATION

Submitted by:

|  | Name(s) and address(es) of legal entity or entities submitting this tender |
| --- | --- |
| Tenderer |  |
| Legal representative |  |
| VAT/Registration number |  |
| Address |  |
| Telephone/ e-mail |  |
| Contact person |  |

- TENDERER’S STATEMENT

I undersigned hereby confirm that the supplies offered in this tender are in full conformity with the specifications submitted to us by the contracting authority. The detailed description of the offered supplies by us is provided in the next point.

In addition to that we confirm that our organisation/company is fully eligible for providing services under a contract financed by the EU funds. We confirm that we are not in any of the situations that would exclude us from competing in the EU financed tenders as indicated in the point 2.3.3. in the PRAG Manual.

Furthermore we agree to abide by the ethics clauses in Section 2.4.14 of the PRAG Manual and have no conflict of interests or any equivalent relation with the Contracting Authority.

- TECHNICAL AND FINANCIAL OFFER

The tenderers are required to provide technical offer, based on the requirements indicated by the contracting authority in the Part A: Information for the tenderer, Point 2: Technical information.

The tenderers are encouraged to provide details on the planned supplies, including detailed specifications and/or brand names.

| No. | No. of items | Title of item | Technical offer – items offered by the tenderer, based on the contracting authority’s requirements in the Part A, Point 2 | Unit cost | Total cost (no. of items x unit cost) |
| --- | --- | --- | --- | --- | --- |
| Supplies |  |  |
| 1.1. | 5 | Examples: desk top computers |  |  |  |
| 1.2. | 5 | Examples: printers |  |  |  |
| 1.3. | 1 | Examples: motor vehicle |  |  |  |
| Installation (*- use this section only when necessary) |  |  |
| 2.1. |  | Examples: Installation of computers (Item no 1.1.) into existing network |  |  |  |
| Other (*- use this section only when necessary) |  |  |
| 3.1. |  | Examples: Manuals of instructions |  |  |  |
| Total price |  |  |  |  |  |

The offered total price for the supplies indicated in the previous point is: <XXX EUR/ national currency>.

Note:

For Romanian beneficiary: Price must be presented in amount including all duties and taxes (e.g. VAT and all other taxes)

For Serbian beneficiary: Price must be presented in amount excluding all duties and taxes (e.g. VAT and all other taxes)

The offered price includes <implementation/delivery> of described items as well as all accompanying costs (for example transport, logistics, material costs) when required.

| Name |  |
| --- | --- |
| Signature |  |
| Date |  |

# EVALUATION REPORT

Reference number: 6/RORS365/Local Council of Moldova Noua

Maximum available budget: <XXX > EUR equivalent < XXX > National Currency (RON or RSD) calculated using the Inforeuro exchange rate from <month of launching the tender procedure>.

The tender submission deadline was <dd/mm/yyyy>.

The evaluation is implemented by the Contracting Authority (CA), represented by the Evaluator(s) <Evaluator 1’s name and surname>, <Evaluator 2’s name and surname>, <Evaluator 3’s name and surname>.

- Administrative check

| Tender envelope number | Tenderer's name | Within deadline? (Y/N) | Tender documentation is complete? (Y/N) | Offer complete and administratively compliant? (Y/N) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| …. |  |  |  |  |  |

2. Technical evaluation

| Envelope number | Tenderer name | Technically compliant (Y/N) | Remarks |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| … |  |  |  |

2. inistrative check

- Financial evaluation

| Tender envelope number | Tenderer's name | Financial offer (EUR/ NC) | The financial offer is within the available budget? (Y/N) | RANKING |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| …. |  |  |  |  |

- Decision

The winning offer is <name of tenderer> for the price of <XXXX EUR/NC>.

Observations: (e.g. correspondence concerning clarifications sought from tenderers)

|  | Name and surname | Signature | Date |
| --- | --- | --- | --- |
| Evaluator 1 |  |  |  |
| Evaluator 2 |  |  |  |
| Evaluator 3 |  |  |  |

# Footnotes

Where applicable. For individuals, mention their ID card or passport or equivalent document - number

The ranking is based on the prices offered – the cheapest technically compliant offer is proposed for contract